## Slide 1: Workshop 3 Presentation: Implementation of Portenta H7 based CAN Bus Simulation & Fault Injection Tool
Nguyen dang tien loi - 21009

## Slide 2: Tool Specifications
- CAN Bus Simulation:
  Classic CAN
  Bit rate 250000
- Fault Injection
  Manipulating Parameters
  Adding Delay
  Ignore

## Slide 3: Hardware Documentations
- Programming using HAL API for:

## Slide 4: Hardware Documentations
- Programming using HAL API for:
  High portability
  Less complex than LL (low level) APIs
  Available for FDCAN (LL not available)
  Offer adequate functionalities over the peripheral
- Peripherals:
  FDCAN1 and SRAM for CAN Bus Simulation
  RTC running by M4 for Fault Injection

## Slide 5: CAN Bus Simulation
- Controller Area Network with Flexible Data Rate (FDCAN)
  The STM32H747 microcontroller offer 2 CAN modules, a shared message RAM and a clock calibration unit
  FDCAN1 also support time triggered CAN
  Message RAM configuration include:
    11-bit filter : filter out standard CAN message
    29-bit filter : filter out extended CAN message
    Rx FIFO 0/1 : store received CAN message
    Rx Buffer : store received CAN message
    Tx event FIFO : stored CAN message to send (ID + timestamp)
    Tx Buffer : store CAN message to send
    Trigger Memory : trigger to send reference message

## Slide 6: CAN Bus Simulation
- FDCAN Config Flow:
  void Set_CAN_Pin(can_t *obj, PinName rd, PinName td, int hz)
    Config CAN pin (following mbed CAN API)
    Call Set_Freq()
  void Set_Freq(can_t *obj, const can_pinmap_t *pinmap, int hz)
    Config Clock for FDCAN1 : PLL1
    Config pin mode for selected Pin
    Config CAN Handle object (CAN CLASSIC + MODE + Bit Timing)
  void Trd_internal_init(can_t *obj)
    HAL_FDCAN_Init() to initialize FDCAN1
    Config & Enable TT operation (COMMUNICATION LEVEL + Trigger Memory)
    Config & Enable TimeStampCounter for interrupt
  int my_can_filter(can_t *obj, uint32_t id, uint32_t mask, CANFormat format, int32_t handle)
    Config Filters and Global Filters
    Activate Notification to enable Interrupts
    HAL_FDCAN_Start()

## Slide 7: CAN Bus Simulation
- Config SRAM
  void init_SDO_object(void)
    Config SRAM handle object and call HAL_SRAM_Init()
    Call write_SDO_to_SRAM()
      Read macros defined in header file to save in SRAM (address = SRAM_BANK_ADDR + WRITE_READ_ADDR + 4*SDO_index) and a linked list SDO object

## Slide 8: CAN Bus Simulation
- Using Interrupts:
  void HAL_FDCAN_RxFifo0Callback(FDCAN_HandleTypeDef *hfdcan, uint32_t RxFifo0ITs): signal receiving new CAN message –> call software algorithm to respond properly
  void HAL_FDCAN_TimestampWraparoundCallback(FDCAN_HandleTypeDef *hfdcan): signal timestamp wraparound to send list of periodic fake CAN message
- Software algorithm procedure
  Read out newly arrived CAN message
  Check whether it is READ or WRITE command
  Read corresponding parameters and send back for READ command

## Slide 9: Fault Injection
- Real-Time Clock (RTC)
  RTC is an independent BCD timer/counter provides a time-of-day clock/calendar with programmable alarm interrupts
  RTC also has a periodic programmable wakeup flag with interrupt capability
  As long as the supply voltage maintains in operating mode, RTC never stops, regardless of the device status (Run mode, low-power mode or under reset)

## Slide 10: Fault Injection
- RTC Config Flow
  void HAL_RTC_MspInit()
    Config clock for RTC and prescaler (if needed)
    Call HAL_RCCEx_PeriphCLKConfig()
    Config and Enable EXTI_LINE_17
    Enable RTC Clock __HAL_RCC_RTC_ENABLE()
  void RTC_Init(void)
    Config Instance and Init object of the RTC handle object
    Call HAL_RTC_Init()
  void RTC_CalendarConfig(void)
    Config TimeTypeDef and DateTypeDef of RTC
    Call HAL_RTC_SetTime()
    Call HAL_RTC_SetDate()
  void RTC_AlarmConfig(uint8_t second)
    Set alarm time
    Call HAL_RTC_SetAlarm_IT()

## Slide 11: Fault Injection
- Scenario Object
  INPUT_TYPE _input_type;
  OUTPUT_TYPE _output_type;
  // input
  CAN_Message *_input_CAN_message;
  uint32_t _input_timestamp;
  // output
  CAN_Message *_output_CAN_message;
  uint32_t _output_timestamp; // for delay
  My_Function *_output_function; // for manipulating parameter
  uint32_t _duration;

## Slide 12: Fault Injection
Work flow:
  Base on declared Scenario Object
  RTC will interrupt (alarm interrupt)
  Base on Type of Input, Type of Output, parameter will be modified or delay will be added or ignore flag will be set