Workshop 3 Presentation: Implementation of Portenta H7 based CAN Bus Simulation & Fault Injection Tool
Nguyen dang tien loi - 21009

---
Tool Specifications
Tool Specifications
- CAN Bus Simulation:
  - Classic CAN
  - Bit rate 250000
- - Fault Injection
  - Manipulating Parameters
  - Adding Delay
  - Ignore

---
Hardware Documentations
Micro controller

---
Bus Matrix

---
FDCAN peripheral

---
FDCAN HAL Instruction

---
FDCAN Implementation

---
RTC peripheral

---
RTC HAL Instruction

---
RTC Implementation

---
TIMER peripheral

---
TIMER HAL Instruction

---
TIMER Implementation

---
SRAM

---
SRAM HAL Instruction

---
SRAM Implementation

---
Hardware Documentations_clipboard0
Hardware Documentations
- Programming using HAL API for:
  - High portability
  - Less complex than LL (low level) APIs
  - Available for FDCAN (LL not available)
  - Offer adequate functionalities over the peripheral
- - Peripherals:
  - FDCAN1 and SRAM for CAN Bus Simulation
  - RTC running by M4 for Fault Injection

---
CAN Bus Simulation
CAN Bus Simulation
- Controller Area Network with Flexible Data Rate (FDCAN)
  - The STM32H747 microcontroller offer 2 CAN modules, a shared message RAM and a clock calibration unit
  - FDCAN1 also support time triggered CAN
  - Message RAM configuration include:
    - 11-bit filter : filter out standard CAN message
    - 29-bit filter : filter out extended CAN message
    - Rx FIFO 0/1 : store received CAN message
    - Rx Buffer : store received CAN message
    - Tx event FIFO : stored CAN message to send (ID + timestamp)
    - Tx Buffer : store CAN message to send
    - Trigger Memory : trigger to send reference message

---
CAN Bus Simulation
CAN Bus Simulation
- FDCAN Config Flow:
  - void Set_CAN_Pin(can_t *obj, PinName rd, PinName td, int hz)
    - Config CAN pin (following mbed CAN API)
    - Call Set_Freq()
  - void Set_Freq(can_t *obj, const can_pinmap_t *pinmap, int hz)
    - Config Clock for FDCAN1 : PLL1
    - Config pin mode for selected Pin
    - Config CAN Handle object (CAN CLASSIC + MODE + Bit Timing)
  - void Trd_internal_init(can_t *obj)
    - HAL_FDCAN_Init() to initialize FDCAN1
    - Config & Enable TT operation (COMMUNICATION LEVEL + Trigger Memory)
    - Config & Enable TimeStampCounter for interrupt
  - int my_can_filter(can_t *obj, uint32_t id, uint32_t mask, CANFormat format, int32_t handle)
    - Config Filters and Global Filters
    - Activate Notification to enable Interrupts
    - HAL_FDCAN_Start()

---
CAN Bus Simulation
CAN Bus Simulation
- Config SRAM
  - void init_SDO_object(void)
    - Config SRAM handle object and call HAL_SRAM_Init()
    - Call write_SDO_to_SRAM()
      - Read macros defined in header file to save in SRAM (address = SRAM_BANK_ADDR + WRITE_READ_ADDR + 4*SDO_index) and a linked list SDO object

---
CAN Bus Simulation
CAN Bus Simulation
- Using Interrupts:
  - void HAL_FDCAN_RxFifo0Callback(FDCAN_HandleTypeDef *hfdcan, uint32_t RxFifo0ITs): signal receiving new CAN message –> call software algorithm to respond properly
  - void HAL_FDCAN_TimestampWraparoundCallback(FDCAN_HandleTypeDef *hfdcan): signal timestamp wraparound to send list of periodic fake CAN message
- - Software algorithm procedure
  - Read out newly arrived CAN message
  - Check whether it is READ or WRITE command
  - Read corresponding parameters and send back for READ command

---
Fault Injection
Fault Injection
- Real-Time Clock (RTC)
  - RTC is an independent BCD timer/counter provides a time-of-day clock/calendar with programmable alarm interrupts
  - RTC also has a periodic programmable wakeup flag with interrupt capability
  - As long as the supply voltage maintains in operating mode, RTC never stops, regardless of the device status (Run mode, low-power mode or under reset)

---
Fault Injection
Fault Injection
- RTC Config Flow
  - void HAL_RTC_MspInit()
    - Config clock for RTC and prescaler (if needed)
    - Call HAL_RCCEx_PeriphCLKConfig()
    - Config and Enable EXTI_LINE_17
    - Enable RTC Clock __HAL_RCC_RTC_ENABLE()
  - void RTC_Init(void)
    - Config Instance and Init object of the RTC handle object
    - Call HAL_RTC_Init()
  - void RTC_CalendarConfig(void)
    - Config TimeTypeDef and DateTypeDef of RTC
    - Call HAL_RTC_SetTime()
    - Call HAL_RTC_SetDate()
  - void RTC_AlarmConfig(uint8_t second)
    - Set alarm time
    - Call HAL_RTC_SetAlarm_IT()

---
Fault Injection
Fault Injection
- Scenario Object
  - INPUT_TYPE _input_type;
  - OUTPUT_TYPE _output_type;
  - // input
  - CAN_Message *_input_CAN_message;
  - uint32_t _input_timestamp;
  - // output
  - CAN_Message *_output_CAN_message;
  - uint32_t _output_timestamp; // for delay
  - My_Function *_output_function; // for manipulating parameter
  - uint32_t _duration;

---
Fault Injection
Fault Injection
Work flow:
  - Base on declared Scenario Object
  - RTC will interrupt (alarm interrupt)
  - Base on Type of Input, Type of Output, parameter will be modified or delay will be added or ignore flag will be set

---
Hardware Documentations
- Programming using HAL API for:
  - High portability
  - Less complex than LL (low level) APIs
  - Available for FDCAN (LL not available)
  - Offer adequate functionalities over the peripheral
- - Peripherals:
  - FDCAN1 and SRAM for CAN Bus Simulation
  - RTC running by M4 for Fault Injection